## Slide 1: Status of the Radiation Effects Facility at the Texas A&M University Cyclotron Institute
Henry L Clark, PhD
Accelerator Physicist / Project Manager
http://cyclotron.tamu.edu/ref/

## Slide 2
Typical Beam Schedule:
1 - 3 weeks SEE Testing (yellow)
1 – 3 weeks of Science Experiments (all other colors)
Schedule 6 – 8 weeks in advance
Two Cyclotrons to schedule….
4 modes of Science/SEE operation

## Slide 3
Mode 1
K500 – Science
K150 – Science

## Slide 4
Mode 2
K500 – SEE
K150 – Science

## Slide 5
Mode 3
K500 – Science
K150 – SEE

## Slide 6
Heavy ions – K500 Cyclotron
Protons &
Heavy ions – K150 Cyclotron
Mode 4
K500 – SEE
K150 – SEE

## Slide 7
Chart: K500 Operating Hours (~8,700h/yr)
| Science (2,900h) | SEE (3,500h) | Devel (800h) | Maint (1,200h) | Down (300h)
K500 Cyclotron Operating Hours (~8,700h/yr) | 3.5632 | 3.5632 | 1.1494 | 1.3793 | 0.34483
ECR Ion Source Change Over

## Slide 8
K500 + K150 SEE Hours at Texas A&M
High Energy Beams & In –Air Testing
Low Energy Beams
50,092 hours over 24 years
K150 REF
Notes: 8

## Slide 9
K500 Cyclotron Heavy-ions beams
95% - 15 MeV/u ions
4% - 25 MeV/u ions
1% - 40 MeV/u ions

## Slide 10
15 MeV/u Au, Xe, Ag are most requested

## Slide 11
Chart: K150 Operating Hours (~8,700h/yr)
| Science (3,000h) | Idle & SEE (1,500h) | Devel (2,000h) | Maint (1,500h) | Down (700h)
K150 Cyclotron Operating Hours (~8,700h/yr) | 3.4483 | 1.7241 | 2.2989 | 1.7241 | 0.8046
Real Beam Development Time
Proton beams

## Slide 12
K150 SEE Hours at Texas A&M
K150 used for 1st Science Experiments
956 hours over 4 years
K150 REF
Notes: 12

## Slide 13: K150 Cyclotron REF Details:
6 - 45 MeV protons (tunable/mono-energetic)
Energy (RF system) changes ~30 minutes
Energy degrader wheel for fast energy changes
Flux adjustable between 1E2 – 1E10 p/s-cm2
Uniform beam spots – 1”, 1.5”, 1.75” dia. (can be reduced to ¼” dia. with collimators)
In-air testing station – 10” x 10” frame remotely controlled (x, y, z, , roll angle)
New sliding shield door for fast access
New Data Room, Setup Area and Equipment
Can be scheduled with K500 Beam Time
15 MeV/u Heavy Ions…..coming soon!

## Slide 14
K150 Cyclotron
Ne, N, He not shown
Start at 12, 10 MeV/u Xe, Ag?

## Slide 15: Biggest Challenges Moving Forward:
How to offer most beam time possible:
  K500 – 2nd ECR will reduce time lost to change over from Science beams to SEE beams
  Utilize both K500 & current K150 beams offered
K150 Cyclotron Vacuum Development:
  Higher vacuum is most important feature to heavy ion development
  Add more external pumps? (Easiest)
  Continue with LHe cryopanel system? (Expensive)
  Break Cyclotron apart & replace O-rings? (Scary!)
  Add more trained staff for additional shiftwork

## Slide 16: Masters in Radiation Effects at Texas A&M:
Two year MS program Physics/Cyclotron Institute:
  Coursework on relevant Physics/EE/ME topics
  Lab work training – conduct SEE testing on well known parts (setup, take data, analyze)
  Masters project – new part type, new technology, new testing procedure….TBD
Masters Project(s) – open to collaborative effort with any agency or company.
Masters Students would graduate with:
  General knowledge in Radiation Effects
  Hands on testing/laboratory experience

## Slide 17: Visit our website at http://cyclotron.tamu.edu/ref/ Questions, contracting, scheduling contact Henry Clark at clark@comp.tamu.edu