## Slide 1: Neutron Ball Testing Part II
Comparing new Cave 4 configuration with old one
090418

## Slide 2
Andrea Jedele Progress in Research Cyclotron Institute
Cave 4 Configuration

## Slide 3
Andrea Jedele Progress in Research Cyclotron Institute
Cave 4 Configuration

## Slide 4
Andrea Jedele Progress in Research Cyclotron Institute
Cave 4 Configuration

## Slide 5
Andrea Jedele Progress in Research Cyclotron Institute
Cave 4 Configuration

## Slide 6
Andrea Jedele Progress in Research Cyclotron Institute
Cave 4 Configuration

## Slide 7
Andrea Jedele Progress in Research Cyclotron Institute
Cave 4 Configuration

## Slide 8: Introduction – Neutron Ball
6 segments/tanks
Filled with EJ-335 (pseudocumene and mineral oil) doped with 0.25% wt. nat. Gd
20 PMTs
  4 top
  12 middle
  4 bottom
Beam
direction

## Slide 9: How does the Neutron Ball Work?
Neutrons enter tank
Neutrons interact with liquid
  Thermalized
Thermalized n are captured by Gd
  Emits several gamma rays (1-2 MeV range)
Pseudocumene scintillates
  Photons are collected in PMTs

## Slide 10: NBL testing
Test the new cave configuration Ar-40 beam @ 24.8 MeV/nuc
Used a Si detector as a trigger
6 consecutive 100 μs gates
Neutron Ball
Nstars Chamber
Si Detector
Target
Tuning
quads
Beam
dump
Half
wall

## Slide 11: NBL testing
600 nA on beam dump
8,000 counts/sec w/o beam
10,000 counts/sec through a blank target
Results show a multiplicity of 7-9 neutrons with a 55% efficiency
Neutron Count |  |  |  |  |  |  | 
Attenuation | 1st window | 2nd window | 3rd window | 4th window | 5th window | 6th window | Δx = (x1-())
1 x 10-2 | 10.96 0.15 | 2.35 0.09 | 2.13 0.08 | 2.00 0.08 | 1.91 0.08 | 2.16 0.10 | 8.85 0.17
10-2 - ps off | 11.02 0.11 | 4.39 0.11 | 4.36 0.11 | 4.22 0.11 | 3.90 0.09 | 4.18 0.11 | 6.81 0.14
3 x 10-3 | 9.63 0.24 | 1.77 0.12 | 1.84 0.16 | 2.29 0.22 | 2.00 0.18 | 1.91 0.19 | 7.67 0.30
1 x 10-3 | 9.02 0.17 | 2.21 0.17 | 2.15 0.16 | 2.20 0.16 | 2.14 0.16 | 1.84 0.13 | 6.91 0.23
3 x 10-4 | 8.56 0.24 | 1.76 0.17 | 2.14 0.22 | 1.97 0.27 | 1.84 0.17 | 1.82 0.20 | 6.65 0.32
Neutron Count |  |  |  |  |  |  | 
Attenuation | 1st window | 2nd window | 3rd window | 4th window | 5th window | 6th window | 
1 x 10-2 |  |  |  |  |  |  | 
10-2 - ps off |  |  |  |  |  |  | 
3 x 10-3 |  |  |  |  |  |  | 
1 x 10-3 |  |  |  |  |  |  | 
3 x 10-4 |  |  |  |  |  |  | 
Neutron Ball
Nstars Chamber
Si Detector
Target
Tuning
quads
Beam
dump
Half
wall

## Slide 12: Beam Shielding studies
More shielding is better
Beam Shielding Effects - Neutron Count |  | 
Beam Shielding | 1st window | 2nd window
No shielding | 8.86 0.13 | 2.89 0.16
1 layer of green board bags | 8.76 0.07 | 2.63 0.07
2nd layer of bags and 1 layer upstream | 8.67 0.12 | 2.35 0.10
2nd layer of bags upstream | 8.48 0.11 | 2.58 0.12
Lead brick wall upstream of bags | 8.80 0.08 | 2.61 0.09
Beam Shielding Effects - Neutron Count |  | 
Beam Shielding | 1st window | 2nd window
No shielding |  | 
1 layer of green board bags |  | 
2nd layer of bags and 1 layer upstream |  | 
2nd layer of bags upstream |  | 
Lead brick wall upstream of bags |  | 

## Slide 13: Beam pulser vs phase shifter
Beam pulser:
  Deflects beam in injection line
  50 μs
  Most within 40 μs
Phase shifter:
  Changes phase of cyclotron
  100 μs
  Most within 80 μs
(ms)
(ms)

## Slide 14: NBL testing K150
Ne-22 beam @ 19 MeV/nuc w/ 10% efficiency 0.3 nA on FC02
In July
  1,000 counts/sec
  ~2,000 counts/sec through blank target
  60,000 counts/sec on 5.0 mg/cm2 Sn target
In September
  1,000 counts/sec
  6,000 counts/sec through blank target
  200,000 counts/sec on Sn target