## Slide 1: The Active Target Time Projection Chamber
D. Bazin
Facility for Rare Isotope Beams
Michigan State University

## Slide 2: AT-TPC @ SOLARIS and now @ HELIOS!
Active Target Time Projection Chamber
Solenoidal Spectrometer Apparatus for Reaction Studies

## Slide 3: Two dual-mode solenoidal spectrometers
Complementarity of detector setups
  Si-array for > 104 pps
  AT-TPC for < 104 pps
Complementarity of facilities
  FRIB + ReA6 for isotopes far from stability
  ATLAS + RAISOR for isotopes ±1n ±2n
SOLARIS @ FRIB
HELIOS @ ATLAS

## Slide 4: Key advantages of the AT-TPC
High luminosity without loss of resolution
  Typical thickness ~10 mg/cm2 compared to usual 100 µg/cm2
  Solid angle coverage ~80%
Several reaction channels measured simultaneously
Determination of reaction vertex
  Correct kinematics for energy loss
  Measure excitation functions
Pure gas operation
  No background from 12C or other target support component
Use of magnetic field in parallel configuration
  Bending of trajectories enable PID and longer tracks within gas

## Slide 5: Main challenges of AT-TPC
Gas target suitable for electron amplification
  New micro-pattern technologies
  Pure gas operation for H2, D2, He, …
Unreacted beam region
  Large amount of deposited charge
  Efficient trigger generation
Data analysis
  Event classification and reaction identification
  Extraction of physical parameters from 3D images of trajectories
Examples of 10Be(d,p)11Be events

## Slide 6: Pure gas operation
Electron avalanche preamplifiers
  Multi-layer Thick Gas Electron Multipliers
  Transmission devices
  Developed by M. Cortesi
  Placed in front of the Micromegas + pad plane
Routine operation in pure H2, D2, Helium, CO2
  Balance between MTHGEM and Micromegas
  Other gases to be tested (mixtures D2 + C4D10, etc…)
M. Cortesi et al., Rev. Sci. Instrum. 88, 013303 (2017)
See talk by M. Cortesi

## Slide 7: Beam region challenges
Large charge deposition on beam region pads
  Induces signal on all other pads via capacitive coupling via mesh
  Large current collected on mesh creates voltage drop
  Pads with saturated signals induce large cross-talk in electronics
  Solution: reduce or eliminate signals from beam region
Trigger generation
  Reaction trigger should avoid unreacted beam signals
  Cannot use mesh signal
  Multiplicity trigger generation subject to cross talk signals
  Solution: reduce or eliminate signals from beam region

## Slide 8: Solution 1: tunable electron avalanche amplification
Micromegas electron amplification
  Proximity of mesh (~ 100 µm) makes electron avalanche localized
  Offers possibility to polarize pads to different potential and change electron gain
“SmartZAP” electronics board
  Arduino micro-controller used to program high voltage shifter chips (HV2801 from Microchip)
  Electron avalanche gain on assigned pads can be varied continuously via external voltage

## Slide 9: Many benefits…
Removal of charge feedback on sensor plane due to mesh coupling
Removal of cross-talk signals from pads located in beam region
Reduce electric field distortions
Possibility to attenuate mesh signal in beam region and use mesh trigger
  Previous experiments used multiplicity trigger with large acceptance cuts
  Pad signal in beam region can still be recorded to get beam track information
Recoiling proton
Scattered 11Be escapes from beam region
Beam region with reduced gain on Micromegas
Cross-talk from saturated pads outside beam region

## Slide 10: Solution 2: pad plane with a hole!
Blind beam region
  3 cm diameter hole
  Both pad plane with micromegas and MTHGEM
  Aluminized mylar foil installed on the MTHGEM to collect electrons
Additional advantages
  Beam can be injected through pad plane
  Zero degree detector or spectrometer

## Slide 11: AT-TPC coupled to the S800
AT-TPC turned around with 4cm window on cathode end to let unreacted beam and beam residues in the S800
Used in first (d,2He) charge exchange experiment using high energy 14O beam on pure deuterium target
  2He decay clearly identified in coincidence with 14N recoil in S800
Rates up to 700,000 pps inside the blind beam region were achieved during experiment e18008
Incoming beam
Beam-like recoil
Target-like recoil
See talk by Z. Rahman

## Slide 12: Data analysis challenges
3D point cloud extraction from trace analysis
Grouping of points into clusters corresponding to individual tracks
Determination of track multiplicity and reaction vertex location
Fitting of individual tracks from modeled trajectories
Extraction of physical quantities
Identification and filtering of events of interest
Machine Learning
Techniques
Machine Learning
Techniques

## Slide 13: Parallel analysis
Two main frameworks used for analysis
  Igor Pro - based (FRIB/MSU)
  Root - based (U. Of Santiago)
  Use slightly different algorithms and functions
  Very useful to cross check issues and share solutions
Main areas of needed progress
  Classify events prior to heavy processing (machine learning techniques on 3D clouds)
  Isolate tracks within point cloud (clustering)
  Fitting of tracks to obtain best resolutions
  Understand main resolution limitations (simulations)
Clustering algorithm developed for AT-TPC data
Dalitz et al., Comp. Phys. Comm. 235 (2019) 159-168

## Slide 14: Analysis demo (1)
Typical proton event
Creation of 3D cloud point from traces
Some cross talk points in the vicinity of the Bragg peak

## Slide 15: Analysis demo (2)
Most of cross talk points have been removed
Track is broken when particle returns to beam region

## Slide 16: Analysis demo (3)
Clustering algorithm correctly groups points into clusters
Two clusters are found due to the lack of data in the beam region

## Slide 17: Analysis demo (4)
Using least-square circle fits, both clusters are regrouped into a single track
Outer points are used to determine estimate of scattering and azimuthal angles, as well as Brho
dE/dx can be determined on portion of the track
Vertex location guessed as closest point to (x,y) origin

## Slide 18: Analysis demo (5)
Circle fit analysis used as starting guess for the fitting algorithm
This is essential to avoid falling into local minima

## Slide 19: Analysis demo (6)
6-dimensional fit converges on the best determination
Objective function is a weighted average of the minimum distance between data and model
This proton has an energy of 1.96 MeV and scattering angle of 78.6°

## Slide 20: 10Be(d,d) elastic and inelastic scattering
2 hours of data
@ 1000 pps…
Gated on incoming 10Be and scattered deuteron
2+1 (3.37 MeV)
2+3 (7.54 MeV)
Resolution: 300 keV FWHM
See talk by Z. Serikow

## Slide 21: 10Be(d,d) Elastic angular distribution
Large center-of-mass angle coverage
Little to no acceptance corrections within that range
Low energy cutoff comes from size of beam region and trigger threshold (< 1 MeV)
Very good angular resolution (~1°)
Possibility to fit OP model parameters for incoming channel

## Slide 22: Example of 6He + 4He decay of 10Be*
10Be(d,d)10Be*

## Slide 23: Several reaction channels measured simultaneously
Commissioning of AT-TPC @ HELIOS using 14C+p @ 12 MeV/u
Plot shows Elab vs lab assuming proton
  Analysis based on estimate of B using circle least-square fit
  “Energy” scale not correct when recoil is deuteron or triton instead of proton
  Online analysis from ATTPCROOT
14C(p,p)14C
14C(p,p)14C*
14C(p,d)13C
14C(p,d)13C*
14C(p,t)12C
14C(p,t)12C*

## Slide 24: Future upgrades and improvements of AT-TPC
New CoBo board (ZCoBo)
  First 2 prototypes received, ongoing preliminary tests
  SoM from Trenz arriving this month - first full tests
  Firmware from U. Of Warsaw via NDA with MSU
Inner beam region tube with gas recovery system
  Use of expensive gases such as 3He
  Recovery system built and tested, inner tube being designed
Heavy recoil detectors at small angles
  Transmission mode: beam injected through hole in pad plane
  Pair of DSSSD (10x10 cm2) placed outside exit flange
  Detectors ordered, design started

## Slide 25: Inner tube for experiments with rare gases
Effort led by U. of Santiago (Spain)
Limitations
  Target-like recoil energy large enough to traverse the thickness of the tube
  (3He,p) is a good candidate
Challenges
  Gas recovery system needed
  Differential pressure regulation with respect to the detector volume
Advantages
  Detector gas can be optimized for performance

## Slide 26: Zero degree heavy recoil detectors
Turn AT-TPC around - inject beam through pad plane hole
Enlarge (now) exit window size to allow greater angular acceptance
Two 128x128 DSSSD: 500 µm & 1 mm
Readout via GET electronics and polarization using smartZAP
Backed by array of 3x3x2 CsI
Further selection of reaction channels
Essential when using AT-TPC without magnet or spectrometer
Radioactive beam
Box containing
DSSSD Si detectors
Target-like
recoil particle
stopping in gas
Beam-like
recoil particle
escaping active volume
Design by
A. Davis

## Slide 27: Latest AT-TPC gallery

## Slide 28: AT-TPC collaboration