## Slide 1: The SPiRIT TPC for heavy ion collision experiments at RIKEN-RIBF
Tadaaki Isobe (RIKEN Nishina Center)
TPC2023 Workshop at Texas A&M University
May 17th 2023
Notes: アニョハセヨ
ネイ、イレムン、イソベイブニダ
36min

## Slide 2: Heavy Ion Collision Exp. w/ TPC to study the density dependent symmetry energy
EOS of pure neutron matter
Large uncertainty on nuclear symmetry energy at r≫r0 compared with that for r≦r0 region.
Heavy ion collision is currently unique way to produce high dense matter in the laboratory.
New experimental project at RIBF for the study of density dependent symmetry energy. r~1.5-2r0 nuclear matter at RIBF energy HIC.
Sn+Sn IBUU
?
?
?
PRC71 (2005) 0146a08

## Slide 3: Collaboration for Device at RIKEN-RIBF: SPiRIT SAMURAI Pion Reconstruction and Ion Tracker
Collaboration formed in 2009
First experiment in 2016
First physics paper in 2021

## Slide 4
RIPS
60~100 MeV/nucleon
~5 MeV/nucleon
350-400 MeV/nucleon
Old facility
New facility
RIKEN RI Beam Factory (RIBF)
BigRIPS
SRC
RILAC
AVF
RRC
fRC
IRC
Experiment facility
Accelerator
SHARAQ (CNS)
SAMURAI
ZeroDegree
SLOWRI
SCRIT
RI-ring
SHE
Z=113
  Intense (80 kW max.) H.I. beams (up to U) of 345AMeV at SRC
  Fast RI beams by projectile fragmentation and U-fission at BigRIPS
  Operation since 2007
<10 MeV/nucleon
CRIB (CNS)
GARIS

## Slide 5
Super Ring Cyclotron
To accelerate Uranium ion to 345 AMeV.

## Slide 6
High-resolution
beam line
F0-F11: 125.983m
ZeroDegree
SHARAQ by U. of Tokyo
SAMURAI
BigRIPS
Max. rigidity = 9Tm
Max. rigidity
=6.8Tm max.
Field integral =7Tm
Fragment separation and PID

## Slide 7
High-resolution
beam line
F0-F11: 125.983m
ZeroDegree
SHARAQ by U. of Tokyo
SAMURAI
BigRIPS
Max. rigidity = 9Tm
Max. rigidity
=6.8Tm max.
Field integral =7Tm
SAMURAI Spectrometer
Superconducting Analyzer for Multi particles from Radio Isotope Beams
B<3T
R: 1m
Gap: 80cm

## Slide 8
80cm
53cm
E field
B field
x
y
NIMA 784 (2015) 513
SPiRIT-Time Projection Chamber
for the measurement of charged particles in HIC
SAMURAI dipole magnet
dE/dX – Br particle identification.
Readout with ~12000 pads.
Operation under B~0.5T

## Slide 9: The SPiRIT TPC
Based on Bevalac EOS TPC.
Wire amplification with P10 gas (1atm).
Target at the entrance of chamber.
~12000 readout pads. 12x8 mm2
Multiplicity: 10~100.
Beam passes through chamber as well.
Rev. Sci. Instrum. 92, 063302 (2021)

## Slide 10: Readout Electronics for TPC: GET
48 AsAds, 12 CoBos, 2 MuTANTs, 2 mTCA shelf
2 DAQ servers with 100 TB RAID array in total.
  Used as cache of raw data  HPC in RIKEN
NARVAL(GANIL) as DAQ software.
  Soap server to control RIBF DAQ
Checking the connection one board by one board.
NIMA 887 (2018) 81, NIMA 899 (2018) 43

## Slide 11: SPiRIT dayone experiment setup
NeuLAND
STQ
MWPC type
Time Proj.
Chamber
12k channel
beam
Chamber in SAMURAI magnet B=0.5T
Beam Tracker

## Slide 12: Trigger system for high dense matter #hits(side)>4 && Z<20
Multiplicity Trigger Array
Multiplicity Trigger Array
Krakow Veto and Trigger Wall
Suppress background events and take “central” collision events
  The fraction of events that we are interested in is only O(0.1)%
Sophisticated trigger system to take central collision data: side array + Forward VETO.
“Spectators”
“Participants”
Low Z
nuclei
n
n
p
p
b
Impact parameter b (fm)
NIMA 856 (2017) 92, NIMA 1039 (2022) 167010

## Slide 13
Cosmic ray in magnet

## Slide 14: Cleaning up experimental area
5 sec./frame. No cut ! It was ~2.5 hour.

## Slide 15: Dayone Heavy RI Collision experiment
Systematic measurements of multiple observables in heavy RI collisions in same Z (Z=50) but different N system.
  Charged pion is main observable.
Successfully finished. 2016 Apr. – Jun.
  Beam rate: 10kHz, trig. rate: 70Hz
  30M Events: 60Hz, 5MB/eve 300MB/sec
  250TB/2week
  Selective digitization/zero suppression was not employed.
Primary | Beam | Target | Ebeam/A | (N-Z/A)sys
238U | 132Sn | 124Sn | 270 | 0.22
 | 124Sn | 112Sn | 270 | 0.15
124Xe | 108Sn | 112Sn | 270 | 0.09
 | 112Sn | 124Sn | 270 | 0.15
A/Q(A.U.)
Z(A.U.)
Beam PID (132Sn)

## Slide 16: First Physics Run at 2016 spring
Feb, 2014
Milestones
1 pixel: 1 pad
TPC Event Display

## Slide 17: Dead channels along beam trajectory
Seen along beam trajectory  due to d-ray?
 but d-ray is supposed to be suppressed with Gating Grid (GG) + B-field.
Could not be seen in the case of cosmic
Location varies event by event

## Slide 18: d-ray which cannot be blocked with Gating Grid (GG)  Preamp becomes dead for a certain time due to large signal of multiple d-ray
Reaction event
GG
Top view
Top view
Side view
Side view
Beam event

## Slide 19: Offline analysis: Charged particle tracking
Pulse Shape Analysis
  in each of 12096 pads
Helix tracking: 3D momentum
  Track separation
  Riemann fit: 2D
  Helix fit: 3D
  Clustering Hits
  Initialize GENFIT parameters
GENFIT: precise fitting (Parameterization, extrapolation)
RAVE(Reconstruction vertices)
t0: time at 5% of h
f: Fixed shape
NIMA 965 (2020) 163840

## Slide 20: Pad Desaturation to recover PID and momenta of particles with saturated pads
Goal: extend the dynamic range of the TPC
Problem: saturated pads lose charge info
2950
3500
650
150
How do we correct and use the PRF?
From the charge pads the distribution we can estimate the charge of a saturated pad
Find the charge center of gravity
Calculate the distance of the center of each pad from the c.o.g.
Calculate the fraction of charge of the pad over the total charge to get the PRF.
NIMA 944 (2019) 162509

## Slide 21: Pad Desaturation
Test performed on the E=100-300MeV Z=1-3 cocktail beam
Overlap of energy loss calculation (Bichsel curves) with data
Before correction
After correction
p
d
t
3He
4He
7Li
6Li
p
d
t
3He
4He
7Li
6Li
NIMA 944 (2019) 162509

## Slide 22: Particle trajectories are distorted due to the large amount of charge made by HI beam
Z~50 10kHz beam: p 25MHz beam
Electrons from beam distort the E-field around beam trajectory
Electrons from produced particles are displaced.
Left hand side trajectories and right hand side trajectories are displaced mainly around vertex.
Drifting
ions made by beam
NIMA 959 (2020) 163477

## Slide 23: Particle identification by TPC 132Sn + 124Sn Ebeam=270 AMeV
p
d
t
4He
6He
3He
7Li
6Li
p+
p-
Z=1

## Slide 24: Reconstruction of vertices: junk event removal
Vertex finding by RAVE package (Reconstruction in an Abstract Vertices Environment)
On the 124Sn target
Start of
TPC
Active
Veto
End of
beam pipe
Target
holder
Inside TPC
Vertices are reconstructed as 3D points at the converging point of the tracks event by event.
Vertexing efficiency 99.3%
On target
Before target
Active target

## Slide 25
F0-F11: 125.983m
BigRIPS
Next step of RIBFDAQ : performing several experiments simultaneously
Upgrade BigRIPS DAQ so that multiple trigger from different experiments can be accepted without interference.
Plastic
PPAC
MUSIC
DAQ for RI beam PID
 no dead time
Common Devices
Trigger
Data
Trigger
Data
Trigger
Data
Courtesy of Baba

## Slide 26: Development of TPC-FEE based on SAMPA chip
R&D within Japanese high/low energy nuclear physics community for next generation TPC readout.
  motivated by the discontinuity of GET system.
To adapt for streaming readout.
Designing of prototype board is on going
  Both triggered and trigger less mode are available by changing the FW.
4 SAMPA chips
Artix Ultrascale+
SFP+ x2
Ext. trigger from User IO

## Slide 27: SAMPA chip feature (v4)
SAMPA = 32 ch * (CSA + Shaper + FADC) + DSP
CSA (pos/neg input) + Shaper: see table
FADC (10bits) sampling: 5, 10, and 20MHz.
DSP functions:
  Data buffering and packeting (header etc.)
  Three baseline correction (restoration) schemes
  Data reduction schemes are simple zero-suppression (ZS), cluster-sum after ZS applied, and Huffman compression (Never used)
Operation mode
  Triggered and trigger-less (continuous) readout mode
  Direct ADC serialization
Output: 11 e-links per chip.
  320Mbps per line  3.2Gbps per chip
  10MHz sampling without zero-suppression is possible
Power: ~1W per chip

## Slide 28: Summary
Experimental program of SPiRIT to constrain the density dependent symmetry energy.
  TPC with readout system of GET.
First experiment campaign by using Sn isotopes was successfully finished at 2016.
  132Sn+124Sn, 108Sn+112Sn, … @E/A=270MeV
Correction of charge saturated hits based on PRF.
Dynamic range of electronics can be gained by using slope information instead of height of signal.
Distortion of particle trajectories due to the large amount of charge made by HI beam.
R&D with SAMPA chip is on-going.