## Slide 1: Studying Fission near 198Pb with AT-TPC at FRIB
Curtis Hunt

## Slide 2: Outline
Fission in AT-TPC
  Interest in Fission
  Method
Setup
  AT-TPC
  HEavy ISotope Tagger (HEIST)
Challenges
  Finding Window and Pad Plane in Time
  Identifying Fission Events
    Algorithmic Method
    Machine Learning Method
  Space Charge
  Signal Processing
Preliminary Results
Summary

## Slide 3: Fission In AT-TPC
Probe of nuclear structure
  Unexpected region of asymmetry in mass yields near 180Hg
  Our interest is in the transition region near 198Pb
Probe of low-density equation of state
  Compare barrier and mass distributions to different effective interactions
Z
N
Moller P and Randrup J 2015 Phys. Rev. C 91 044316
Notes: 2:15. symmetry energy term at low density. Drew Pype making calculations of potential energy surfaces to compare to experiment.

## Slide 4: Fission In AT-TPC
Goal is to measure fission properties of short-lived isotopes
  Fission barrier, cross-section, asymmetry of fission fragments
Nucleus excited through light ion induced fusion-fission -> low angular momentum
  Fission of compound nucleus
Using an Active Target TPC provides several advantages to the study of fission using fusion-fission
Moller P et. Al. J 2015 Phys. Rev. C 91 024310
Notes: 3:15 In 190Hg, mass asymmetry survives at E* up to 70 of MeV from ANU data

## Slide 5: Fission In AT-TPC
Using an Active Target allows for probing a large range of excitation energies
  Allows for measuring cross section over range of energies with single beam
Active Target allows for accurate determination of reaction vertex and reconstruction of the event
  Vertex used to obtain excitation energy and the angle between fission fragments
Inverse kinematics allows for the use of radioactive isotopes in study of fusion-fission reactions
Inverse kinematics boosts fragments forward
  Fission events form a characteristic Y pattern toward the pad plane

## Slide 6: AT-TPC
AT-TPC (Active Target Time Projection Chamber)
  Reactions occur inside the gas volume of the TPC with the gas
1000 mm long x 250 mm radius cylindrical active volume
10240 micromegas pads
  Perpendicular to beam direction
  Triangular pads
  Highly segmented inner region
Cylindrical design allows for use in magnetic field
  We did not use a magnetic field for fission study

## Slide 7: AT-TPC - GET
Generic Electronics for TPCs (GET)
  AGET chips
    64 data channels + 4 FPN channels
      Fixed Pattern Noise (FPN) channels measure the baseline due to electronics
    Preamplification and Shaping
  AsAd (ASIC and ADC) boards
    4 AGET chips per board
    Digitizes signal from the AGET
  CoBo (Concentration Board) Module
    Up to 4 AsAd per CoBo
  MuTAnT (Multiplicity, Trigger and Time)
    Manages the trigger for the connected CoBos
E.C. Pollacco et al. NIMA 887 (2018) 81-93

## Slide 8: Identifying Rare Isotope Beams
Beams are separated in a magnetic fragment separator
  Puts a very tight cut on rigidity ()
Measure time of flight (ToF) of beam between two fixed points
  Gives the particle velocity ()
Measure energy loss through gas detector ()
Lab not convinced it was possible with lead -> new detector system!
Simulated PID plot
Z: Element number
A: Mass number
q: Charge-state

## Slide 9: HEavy ISotope Tagger (HEIST)
ToF
Adam Anthony
MSU Grad Student

## Slide 10: Experimental Setup
PID system (HEIST)
  MCP and ion chamber
  Si and HPGe support system
Degrader system
  Fe degrader and ion chamber
Active target (AT-TPC)
  4He gas target
  E* from 65 MeV down to 30 MeV
  Trigger on MCP2 and pad plane coincidence
Notes: 5:00 Walk through path of beam, and discuss detectors as you hit them

## Slide 11: Finding Window/Pad Plane Time
Identify pads showing energy deposition near window and pad plane
Fit leading edge of pad traces
  Window: t0 gives time electrons drifted from window reach pad plane
  Plane: t0 gives time fission fragment hits pad plane
Window Fit equation: Empirical estimation for spread from diffusion
Pad Plane Fit equation:
Response function from electronics
A
Bergen Kendziorski
MSU Undergraduate
Pad Plane
Window

## Slide 12: Sorting Fission From Beam
Low gain region in center of TPC should omit beam events
In practice, we still record orders of magnitude more beam than fission
  ~ 2-3% of events are fission events
Algorithm was developed to tag as many unwanted events as possible
  Set of ~2500 hand labeled events was used for development
  Parameters that can be quickly & automatically calculated were found
    Polar angles of straight-line tracks, spread of e- hits recorded in x-y plane, etc.
  Events are either labeled fission, beam, or “other” if parameters are ambiguous
Fission
Beam
Other?
Notes: Consider animations to introduce set up.

## Slide 13: Sorting Fission From Beam: Results
Run: 206
Beam Rate: 3809
Gas: CF4 @ 150 Torr
Run: 261
Beam Rate: 2136
Gas: CF4 @ 200 Torr
“Other”:
25 Fissions 44 Beams
“Other”:
27 Fissions
111 Beams
Events are sorted into “beam”, “fission”, and “other” categories.
~2-3% of all events are sorted into the “other” category
~15-30% of fission events are sorted into “other”
Combining “fission” and “other” categories yield 100% fission event capture with ~30-40% events being beam events
Joe Wieske
MSU Grad Student
Notes: Consider animations to introduce set up.

## Slide 14: Machine Learning Approach To Classifying Fission and Beam Events
Confusion matrix from testing on hand-labeled data from the other category
Use a machine learning model to classify these “Other” events.
  Worked with Michelle Kuchera and Raghu Ramanujan (Davidson College)
Train the model on labeled Fission and Beam events from the algorithmic approach
Apply the trained model to a small subset of hand labeled “Other” events for testing
  81% Fission events in “Other” correctly identified
  ~94-97% Fission events captured with algorithmic + ML methods combined
 | Guess Beam | Guess Fission
True Beam | 902 | 0
True Fission | 6 | 25
Poulomi Dey
MSU Undergraduate
Beam
Fission

## Slide 15: Space Charge: The Problem
Accumulated positive ions (He+) drift much slower than e- because of their significantly lower mobility
  Creates a line of positive charge along the beam path
Some fission fragment tracks curve inward
  Drifting e- are pulled inwards by the resulting ion transverse E-field
  Effect is rate dependent
Results in wider folding angles and reaction vertices offset downstream
  Vertex location gives the excitation energy
  Fragment directions give mass split
Notes: Consider animations to introduce set up.

## Slide 16: Space Charge: How To Correct Distortions
Fission events are fit with “Y-track” to extract observables (vertex, angles)
For certain events we can determine the vertex separately from Y-track
  The lighter fission fragments loose much less energy over distance than the heavier beam, creating a discontinuity in dE/dx
These provide a metric to quantify how well corrections are tuned
  Proper correction will result in vertex agreement between the two methods
***Before correction***
Beam region dE/dx
Notes: Consider animations to introduce set up.

## Slide 17: Space Charge: How To Correct Distortions
Distortions to e- drift path can be modeled by solving Langevin Equation
  Electric field is a combination of the known TPC drift field and the unknown space charge distribution
  Space charge should build up more strongly towards entrance window
Input a model for the space charge distribution, then solve for drift corrections
Notes: Consider animations to introduce set up.

## Slide 18: Space Charge: Correction Results
RED = Before correction
BLUE = After correction
***Example Corrected Event***
Y-Fit Vertex (mm)
Y-Fit Vertex (mm)
ADC Vertex (mm)
Vertex Difference
- Before -
Vertex Difference
- After -
Joe Wieske
MSU Grad Student
Notes: Consider animations to introduce set up.

## Slide 19: Deconvolution – Shaper Effects
When the charge distribution is short relative to the shaper rise time, the total charge is measured by the shaped pulse height
When the distribution is long the pulse height does not represent the total charge
  Fission fragments move toward the pad plane, spending notable distance over a given pad
Input Charge
Output Signal

## Slide 20: Deconvolution – Reconstruction Principle
Output signal, sout(t), is the convolution of input signal, iin(t), and the response function, h(t)
  Channel dependent
The signal can be deconvolved with Fourier transform
With the Fourier transform of the response function the input charge as a function of time can be found
  Need response function
Response function can be obtained from output with known input
J. Giovinazzo et al. NIMA 840 (2016) 15-27

## Slide 21: Deconvolution – Response Function
650 mV internal AsAd pulser test used to get response function
  Pulser signal is recorded by the FPN channels
Deconvolution of the pulser signal did not work due to very few time buckets involved in the signal
  Pulser signal is effectively a delta function
Shaped pulser signal was used as the response function
Pulser Signal
[iin(t)]
Shaped Pulser Signal
[sout(t)]

## Slide 22: Deconvolution – Response Function
The inverted signal messes up the return to zero
Add the positive signal to the negative signal to cancel it out
Some “glitches” needed to be removed and extrapolated
Shifted response function to start at 0 and normalized height to 1
Response Function
[h(t)]
Shaped Pulser Signal
[sout(t)]

## Slide 23: Deconvolution – Results
Deconviolution corrects shape for undershoot due to response function
Gives reliable dQ/dt results for fission fragments
Shaped Signal [sout(t)]
Reconstructed Charge [iin(t)]

## Slide 24: Preliminary Results
Charge asymmetry
  Energy loss of products
    , where varies slowly
  Energy Loss related to mass of particles
- Fragment A
- Fragment B
Time Buckets
Charge
Adam Anthony
MSU Grad Student
Missing pads

## Slide 25: Preliminary Results
Charge asymmetry
  Energy loss of products
    , where varies slowly
  Energy Loss related to mass of particles
- Fragment A
- Fragment B
Time Buckets
Charge
Adam Anthony
MSU Grad Student
Missing pads

## Slide 26: Summary
Fission in AT-TPC
  Experiment looking at fission near 198Pb has been performed with AT-TPC
Challenges Solved
  Beam particle identification
    HEavy ISotope Tagger (HEIST)
  Identifying Fission Events
    Use a combination of algorithmic and machine learning methods
  Space Charge
    Solved Longevin equation to correct fission tracks
  Signal Processing
    Deconvolution for accurate dQ/dt (related to dE/dx)
Preliminary fission fragment asymmetry measurements
  More results, including cross sections, to come
Future
  Use rare isotope beams from FRIB to look at fission of more exotic isotopes

## Slide 27: Questions?
Questions?

## Slide 28: Backup Slides

## Slide 29: Sorting Fission From Beam: Example Parameter

## Slide 30: Sorting Fission from Beam: Results
Run: 210
Beam Rate: 3335
Gas: CF4 @ 150 Torr
Trigger: DS Singles + coinc
Run: 206
Beam Rate: 3809
Gas: CF4 @ 150 Torr
Trigger: DS Singles + coinc
Run: 211
Beam Rate: 6467
Gas: CF4 @ 150 Torr
Trigger: DS Singles + coinc
Run: 260
Beam Rate: 2106
Gas: CF4 @ 200 Torr
Trigger: DS Singles (5000) + coinc
Run: 261
Beam Rate: 2136
Gas: CF4 @ 200 Torr
Trigger: DS Singles (500) + coinc
Run: 271
Beam Rate: 7665
Gas: CF4 @ 200 Torr
Trigger: DS Singles (500) + coinc
“Other” = 25 Fissions 44 Beams
“Other” = 27 Fissions 111 Beams
Notes: Consider animations to introduce set up.

## Slide 31: Deconvolution – Reconstruction Principle
Output signal, sout(t), is the convolution of input signal, iin(t), and the response function, h(t)
  Channel dependent
The signal can be deconvolved with Fourier transform
With the Fourier transform of the response function the input charge as a function of time can be found
Analytical formula for the response function
  A is the amplification gain
  τ is the peaking time
  Analytical formula is not accurate enough for proper deconvolution

## Slide 32: Deconvolution – Baseline Corrections
Pulser tests with internal AsAd pulser were used to obtain response function of the GET preamp and shaper
0 V test to get backgrounds
  Channel dependent baseline
  Phase effect from circular buffer
Baselines usually corrected by FPN channels, but in pulser test FPN channels have the pulser signal

## Slide 33: Iterative Deconvolution
For long signals (such as for the beam) the deconvolution does not reconstruct charge perfectly

## Slide 34: Iterative Deconvolution
Signal can be reconstructed by convoluting the charge with the response function using the summation method
The difference between the source signal and the reconstructed signal is not 0

## Slide 35: Iterative Deconvolution
The difference between the actual signal and the signal from the reconstructed charge can be iteratively used to correct the charge.
  1) Use the deconvolution method on the signal difference to obtain the difference in “charge space” (go from “signal space” to “charge space”)
  2) Subtract the result from the charge and obtain a new reconstructed signal
  3) Calculate the difference between the source signal and new reconstructed signal
  4) Repeat

## Slide 36: Iterative Deconvolution
4 iterations appears to be sufficient to obtain a relatively flat difference

## Slide 37: Observables from AT-TPC
Cross-section
  Energy determined from vertex location
    Space Charge corrections crucial
  Determination of Fission vs Beam
    Standard + ML methods

## Slide 38: Observables from AT-TPC
Cross-section
  Energy determined from vertex location
    Space Charge corrections crucial
  Determination of Fission vs Beam
    Standard + ML methods
Charge asymmetry
  Energy loss of products
    , where varies slowly
    Deconvolution important for charge comparisons

## Slide 39: Simulation of fission events
Simulated fission events
Experimental fission events (all beam species)
Z ~ 32
Z ~ 52
Notes: 26